## Slide 1: A Project to Investigate and Produce Solutions to the Electricity Waste in Bilkent Dormitory 78
Umut m. köksaldı

## Slide 2: Overview
Introduction
Problem Definition
Proposed Solutions
Criteria for Assessing Solutions
Research Methodology
Results and Analysis
Conclusion and Recommendations
References

## Slide 3: Introduction
Dorm 78
  586 students, 236 rooms [1]
Consuming 1582 kWh / day energy
Stanford University Dorms: 1.04 kWh / day for each person [2]
Dormitory 78: 2.69 kWh / day for each person
  ~2.5 x more electricity used by the average dormitory resident

## Slide 4: Problem Definition
Excessive electrical energy consumption inside Dormitory 78
Root cause 1:
  Lack of control mechanisms in the building
Root cause 2:
  Out-dated and worn-out lightbulbs
Root cause 3:
  Unplanned design and installation of the building’s light fixtures

## Slide 5: Proposed Solutions
Solution 1:
  Installing sensors
Solution 2:
  Increasing the efficiency of the light bulbs
    (Replacing with more efficient LED light bulbs)
Solution 3:
  Optimizing the layout of the building’s lighting fixture

## Slide 6: Optimizing the lighting layout

## Slide 7: Taking into account:
The lighting intensity of LED lights should they be installed
Positioning the bulbs closer to walls to benefit from the reflection
Maximize efficiency of one lightbulb while minimizing the quantity of lightbulbs

## Slide 8: Optimized Layout

## Slide 9: Criteria for Assessing Solutions
Cost-effectiveness
  There should be a reasonably satisfactory value (savings) returned from the implemented solutions in relation to the monetary cost of realizing such systems (Return on investment)
Acceptability
  The proposed solutions need to be easy for the students to adapt to, and they should not interfere with the students’ day-to-day life
Feasibility
  The solutions should be technically rational and suitable for the building’s condition (e.g. redesign of the light bulb layout should be possible given the building’s construction)

## Slide 10
Installing sensors | Cost-effectiveness | Calculations of the installment cost and the savings sensors would provide
 | Acceptability | Survey for students, building management interview
 | Feasibility | Interview with Chief Electrical Engineer Türesin Özpineci
Increase efficiency of bulbs | Cost-effectiveness | Calculations and comparisons between fluorescent and LED bulbs
 | Acceptability | Interview with Dormitories Manager Zeki Samatyalı
 | Feasibility | Examining previous similar work
Layout optimization | Cost-effectiveness | Interview with Chief Electrical Engineer Türesin Özpineci
 | Acceptability | Survey for students, building management interview
 | Feasibility | Interview with Türesin Özpineci and Financial Manager Ali Mehmet Kılınç

## Slide 11: Results & Analysis

## Slide 12: Cost-effectiveness of sensors
Approximately 612 lightbulbs for sensors to be installed
Cost of a sensor is 17 ₺, total cost: 10,404 ₺ [3]
  Labor cost: approximately 1000 ₺
Expecting a 40% cut on uptime of bulbs
  1kWh of energy worth ~0.41 ₺ [4]
  Total savings: 2594.48 ₺ per month, break even: 4-5 months

## Slide 13: Acceptability of sensors
Chart: Do you want sensors to be installed to the lighting fixtures inside Dormitory 78
| Yes | No
Do you want sensors to be installed to the lighting fixtures inside Dormitory 78 | 7.4 | 3.6
Dormitory Management: Partially acceptable
Can be implemented alongside other solutions or modificaitons

## Slide 14: Feasibility of sensors
Interview with İbrahim Türesin Özpineci
There are no big adjustments to the electrical grid for the sensors
Enough technical personnel to realize the system
The solution is feasible as long as the supply of sensors is ensured

## Slide 15: Cost-effectiveness of LED lightbulbs
Cost of an LED lightbulb: 15 ₺ [6]
Total cost of replacing 612 bulbs: 9180 ₺
LEDs use up to 50% less energy compared to fluorescent [7]
Total savings: 9729 ₺ per month
  Break even: ~1 month

## Slide 16: Acceptability of LED lightbulbs
Interview with Zeki Samatyalı
The process is simple and does not require too much work
  Can be done overnight
Deemed LED lights ‘the most appropriate solution’
Dormitories Management is on board with the solution

## Slide 17: Feasibility of LED lightbulbs
Case: Stanford University
Stanford has managed to reduce campus-wide electrical energy usage by 25% as a result of LED lights [5]
The process is simple and does not require technical expertise

## Slide 18: Cost-effectiveness of lightbulb layout optimization
~400 lights to be removed and 122 lights to be reinstalled into the ceilings
Labor cost: ~15,000 ₺
Approximately 280 lights removed
  Total savings: 7783 ₺ per month
  Break even: 2 months

## Slide 19: Acceptability of lightbulb layout optimization
Dormitory management does not accept the solution
Management states that the proposed solution is too obstructing for both the students and the dorm staff
Could be implemented if the electrical infrastructure of the building was already being changed

## Slide 20: Feasibility of lightbulb layout optimization
Interviews with Electrical Engineer Türesin Özpineci and Financial Manager Ali Mehmet Kılınç
The proposed solution is too costly from an economic standpoint
Too big of an overhaul of the building’s construction
The solution is not feasible

## Slide 21: Conclusion & Recommendations
Cost-effectiveness
Acceptability
Feasibility
Sensors
LED lightbulbs
Layout optimization
Total

## Slide 22: Recommended action plan
Combination of solution 1 and solution 2
LED lights should be installed primarily and during the construction process sensors should also be implemented into the new lighting fixtures

## Slide 23: References
[1] Bilkent University, ‘Hizmet ve Olanaklar’, 2013. [Online]. Available: http://www.yurt.bilkent.edu.tr/78a.html [Accessed: 26-Jun-2017]
[2] Stanford University, ‘Fact Sheet: Student Housing’, 2016. [Online]. Available: https://sustainable.stanford.edu/sites/default/files/FactSheet_StudentHousing.pdf [Accessed: 23-Jul-2017]
[3] Elektrikmarket.com, ‘Tavan Hareket Sensörleri’, 2017. [Online]. https://www.elektrikmarket.com.tr/Sensor-180-Derece-Beyaz-Horoz-088-001-0003,PR-50780.html [Accessed: 24-Jul-2017]
[4] Gazelektrik.com, ‘Mesken Elektrik kWh Fiyatları’, 2016. [Online]. http://gazelektrik.com/faydali-bilgiler/1-kwh-elektrik-kac-tl [Accessed: 24-Jul-2017]
[5] Stanford University, ‘Advancements in Energy Efficiency’, 2016. [Online]. Available: https://sustainability-year-in-review.stanford.edu/2016/features/advancements-in-energy-efficiency/ [Accessed: 23-Jul-2017]
[6] Vatan Computer, ‘Goldmaster LED AMPUL E27’, 2017. [Online]. http://www.vatanbilgisayar.com/la-127-bl2-led-ampul-e27-duylu-10w-75w-akkor-220v-3000k-sicak-beyaz.html [Accessed: 24-Jul-2017]
[7] Lowes.com, ‘Lightbulb Buying Guide’, 2016. [Online]. https://www.lowes.com/projects/decorate-and-entertain/Lightbulb-Buying-Guide/project [Accessed: 25-Jul-2017]